## Slide 1
OPO Theory of Operation

## Slide 2: Optical Parametric Oscillator
NLO Crystal
Signal
idler
Resonator provides feedback at signal or idler or both
No signal beam required as input
Buildup from noise
No population inversion takes place no energy storage
Single pass gain = single pass loss threshold condition
Pump

## Slide 3: Optical Parametric Process
Energy conservation
EIN = EOUT = E1 + E2
    win = w1 + w2
 Wavelength pairing
l= wavelength
Momentum conservation
  kIN = k1 + k2
   Phase matching
  n=index of refraction
Labeling convention !
  for lin < l1 < l2
  in = Pump, 1 = Signal, 2 = Idler
P=0[(1)E+(2)E E++(3)E E E+]
Param.
Process
(2)
Pump
Signal
Idler
P= Polarization
E= Electrical Field
= optical susceptibility
()= Order

## Slide 4: Tuning Methods of OPOs – II
Tuning Methods: pump tuning
dispersion tuning
OPO with bulk KTP
pump tuning curve
OPO with PP crystal
dispersion tuning

## Slide 5: Dispersion Tuning – PP OPO
time
Dispersive
Glass block
time
nred < nblue
λred
λblue

## Slide 6: Synchronously Pumped Ultrafast OPOs
Synchronously pumped OPO
the length of the OPO is matched to
that of the pump laser resonator
The gain experienced in one pass will be enhanced by
the gain experienced on the subsequent passes
The consecutive coincidence of the parametric and pump wave
amplifies the signal until it overcomes the threshold
TLASER
lOPO

## Slide 7: Femtosecond OPO Schematics
Pricipal OPO scheme
Low pulse energy  pump beam focussing
80 MHz  1.875 m cavity length
80 MHz
1.875 m
OPO
Lens
w0 = 50 µm

## Slide 8: Quasi-Phase-Matching
Periodic change in the sign of the nonlinear susceptibility before the back conversion starts.
The field will be enhanced instead of cancelling during the second half of the cycle
QPM- Quasi-Phase Matching
Advantage: higher non linearity, broader phase-matching range
BPM- Birefringence Phase Matching
NPM- None Phase Matching
Experience back conversion no growth

## Slide 9: Periodically-Poled OPO Crystal
PP-Xtals
  Extremly broad phasematching range
  Fixed pump wavelength (comfortable)
  PC controlled OPO tuning
 Dispersion tuning λSignal ~ LCavity
Quasi Phase Matching:
(Momentum conservation)
: Grating period

## Slide 10: PP Fan Crystal
Crystal structure
  Translation of the crystal leads to continuous poling periode change
  Selection of the proper poling periode for each pump / Signal wavelength combination
900
1000
1100
1200
1300
1400
1500
1600
750
770
790
810
830
850
Pump wavelength / nm
OPO Signal wavelength / nm
Position of
pump beam
L
lSignal
lIdler

## Slide 11: PP Fan Crystal
The fan poled crystal: phase-matching
Example poling periods of a PP MgO:LN crystal for different pump / Signal combinations