## Slide 1: Chameleon Service Training
Dieburg, 06.-10.06.2016
Laser System Overview
Part 2

## Slide 2: Overview
Models & Specifications
VPUF Laser Basics
Differences between 90 & 80 MHz Platforms
Laser Safety Review

## Slide 3: Chameleon Models & Specifications
Chameleon 210nm
Chameleon XR
Chameleon Ultra
Chameleon Ultra 1 & 2
Chameleon Vision 1
Chameleon Vision 2
Chameleon Vision S
Chameleon OPO
New: Chameleon Discovery

## Slide 4: Chameleon & Chameleon XR
XR: Xtended (Tuning) Range

## Slide 5: Chameleon Ultra Family
80 MHz Platform

## Slide 6: Chameleon Vision Family
Vision = Ultra 2 + GDD

## Slide 7: Chameleon Vision Family
Vision-S = Ultra 2 + GDD + shorter pulses

## Slide 8: Chameleon OPO

## Slide 9: New: Chameleon Discovery

## Slide 10: New: Chameleon Discovery
1. Outlet: Tuningrange: 680 – 1300nm
2. Outlet: fix @ 1040nm / 1,5W / 160fs
Pulse Length: 100fs
GDD - Unit
Control via PanelPC

## Slide 11: New: Chameleon Discovery - Specials
DPSS UF Pump Source @ 1040nm
Seed/Amplifier
Internal OPO pumping
Both Outlets are synchronuous 
Ideal for CARS, SRS & Frequency mixing

## Slide 12: VPUF – Laser Basics
VPUF: Verdi Pumped UltraFast Resonator
Passive Pulse generation of a Ti:Sa crystal
  Kerr Lens Modelocking (KLM)
  Self focusing: very high intensity (NLO) changes index of refraction inside crystal
  This changes resonator parameters like divergence & beam waist.
Starter kick for pulse process required.
Wavelength Tuning via BRF (Mira) & Prism shift (Chameleon) possible
  Small window with less losses, large areas with high losses

## Slide 13: Kerr Lens Modelocking (KLM)

## Slide 14: CW-Breakthrough & Q-Switching

## Slide 15: CW-Breakthrough & Q-Switching
REES measurement: Acceptable spectrum

## Slide 16: CW-Breakthrough & Q-Switching
REES measurement: Unacceptable spectra
Q-Switching
CW-Breakthrough

## Slide 17: Tuning Kalibration

## Slide 18: Typical Tuning Curve

## Slide 19: Chameleon Laser Head
Verdi Pumped Ultrafast , VPUF
Cavity power track, CPT
Pump power track, PPT
Output Coupler, OC
VERDI
sealed head
PPT
VPUF, sealed head
Tunable ultra-fast Ti:s cavity
(utilizing Power Pulse system)
CPT
OC
Pump optics

## Slide 20: Chameleon Laser Head – VPUF Cavity
Verdi™ CW green Pump Laser
Active mirror[1]
Active mirror[1]
Ti:S rod
Movement of combined prism/ slit determines GVD (l) and hence t(l). Our choice of axis gives minimal t(l). [2]
Tuning slit
Chameleon
Power Supply / Controller
KLM slit
Photo -diode
Output

## Slide 21: Differences between 90 & 80MHz Platforms
90MHz: 210nm & XR
80MHz: All Ultra & Vision
FSB 468:
1. The physical differences internal and external to the Chameleon
head and power supply.
2. The operational differences from both an operator and a Service
Engineer’s perspective.
3. The changes incorporated with the new Chameleon software.
4. The changes incorporated with the new Chameleon hardware.

## Slide 22: Differences between 90 & 80MHz Platforms
90MHz:
Pumplaser: V10, V12
Analogue Headboard on top of resonator
Black umbilical between PSU & Head
80MHz:
Pumplaser: V18
Digital Headboard beside
Separate cables & fibers
Front Panel User Menu / GUI

## Slide 23: Differences between 90 & 80MHz Platforms
Ultra Digital Head Board

## Slide 24: Differences between 90 & 80MHz Platforms
Ultra: Change to cavity layout

## Slide 25: Operational Differences
90MHz Platform
  Set Temperature is 25°C
  Mirror positions are displayed: 0-5 V
80MHz Platform
  Set Temperature is 25°C
  Significant changes to user & service menu navigation
  Chameleon software in foreground
  Powermap now a software routine
  Mirror positions are displayed: -100% - +100%
  ML slit control

## Slide 26: Recovery / Initialise
Recovery
  90MHz platform only
  Tunes to peak wavelength & scans PZTs for optimum alignment
Initialise
  80MHz platform only
  Tunes to peak wavelength & scans PZTs for optimum alignment

## Slide 27: Function of Pump & Cavity PZT’s
Electronical adjustment of mirror positions
Px, Py: Verdi beam adjustment (x: horizontal, y: vertical)
Cx, Cy: Ti:Sa cavity mirror adjustment

## Slide 28: Pump & Cavity PZT’s
Check of mirror positions on Front Panel & GUI

## Slide 29: Tab Tune: l - Sweep
Mirror optimization  Power increase
Customer accessable

## Slide 30: Laser Safety Review
Service Manual, Section 1.1
Operator Manual, Section 2
Setup: class 1 (fully covered beam), class 4 (open beam)
Setup: table walls, lab windows, curtains, customer goggles
Training: FSE yearly LS training, customer needs “Laser Safety Officer”
Laser Features: Interlocks, Shutter, Warning Lamp

## Slide 31: Laser Safety Features
Three Interlock – Circuits
  Verdi Head Interlock: Laser Emission Lamp
  Power Supply Interlock: Cover open
  External Interlock: MRU, Lab Door,…
Shutter