## Slide 1: PowerLine E 8 QT (AC)
Air-cooled 7 W UV Laser Marker for high-end marking applications

## Slide 2: PowerLine E 8 QT (AC) – At a Glance
Integrated laser rail (class 4) with Matrix 8-355-50 laser source
For integration into Coherent Munich or 3rd party handling systems
Compact design with many standard features:
  180° beam deflection unit
  Positioning laser
  Mechanical safety shutter
  Internal power sensor
  Air recirculation and filtering inside critical optical components
High-end galvanometer scanners and optics
Supply unit (based on Coherent Munich’s PowerLine E - ITX)
Fully air-cooled
VLM / Laser Console software (w/ Matrix 8-355-50 GUI function)
Supports Marking on the Fly, 3D freeform marking etc.
 | PowerLine E 8 QT (AC)
Wavelength | 355 nm
Average Power [@flange] | 7 W (45 kHz)
Average Power [@work piece] | > 6 W (45 kHz)
Frequency Range | 20 - 135 kHz
Pulse Energy | 120 µJ (45 kHz)
Pulse Width | < 25 ns
M2 | < 1.2
Controller | RCU – ITX
Software | VLM 5.3 / Windows 10 IoT Enterprise
Chiller | Air cooling
Dimensions (W x H x L) | 225 x 336 x 819 mm

## Slide 3: Integration Concept
Matrix 8-355-50 Laser Source
Attenuator (optional)
Collimation Lens
Beam Expander
FFM (optional)
Power Senor
(air cooled)
Purification Unit
Scanner
Beam Deflection Unit
(incl. safety shutter)
Positioning Laser

## Slide 4: Coherent Matrix 8-355-50 DPSS UV Laser
30 years of UV manufacturing expertise
Extremely robust industrial design
Head assembly in cleanroom, tight quality control
Installed base > 2,000 worldwide
Warranty return-rate < 3%
Sealed UV compartment with purge

## Slide 5: Typical Power Curve of the PL E 8 QT
First pulse suppression by applying Pulse EQ Mode
Max. output power at 45 kHz: 7 W [@ flange]
Max. output power at 45 kHz: > 6 W [@ marking field]
Output power is adjusted by adjusting resonator charging time.
Chart: Frequency (kHz)
| 135 | 100 | 90 | 80 | 70 | 60 | 50 | 45 | 40 | 30 | 20
PL E 8 QT | 3.52 | 4.51 | 4.95 | 5.44 | 5.99 | 6.3 | 6.8 | 7 | 6.32 | 4.69 | 3.117
PL E 5 QT | 2.19 | 3.19 | 3.54 | 3.89 | 3.92 | 4.11 | 4.3 | 4.5 | 3.72 | 2.11

## Slide 6: All-in-One Supply Unit
Compact 19-inch rack unit, height: 2 RU
Power supply
ITX CPU motherboard (VLM + VMC)
ALI *) board (scanner / laser control board)
Laser controller
Monitoring of laser marker status
  Output power
  Frequency
  Pilot on/off
  Shutter open / close
Error diagnostics
*) Active Laser Interface

## Slide 7: Application Examples
Plastic screw caps
Power: 6.5 W
Scan speed 1,900 mm/s
> 25 caps / s
1.2x Beam expander
0.8x Beam expander

## Slide 8: Marking of Home Applicances
Plastic screw caps
Power: 6.5 W
Scan speed 1,000 mm/s
> 25 caps / s

## Slide 9: Highlights of the PowerLine E 8 QT (AC)
Compact design by using beam deflection unit folding the laser beam.
Standard features integrated into laser head:
  Mechanical shutter for safe laser operation
  Power sensor for monitoring / controling laser output power
  Laser positioning help for localizing the exact marking area
  Beam expander
Fully air-cooled laser marker
Collimated laser beam for easy process setup. Working distance does not depend on beam expansion factor.
Compartments inside laser head for additional optical components
Purification unit circulates and filters air within critical components to avoid undesired opto-chemical reactions.
VLM / VMC software package known from PowerLine E laser markers is included.

## Slide 10: Physical Dimensions

## Slide 11
THANK YOU FOR YOUR ATTENTION
www.coherent.com